## Slide 1: Programming Networks: The New Way to Provide Communications Services Managing Next Generation Mobile Systems
James Irvine Mobile Communications Group Strathclyde University

## Slide 2: Basic Mobile Phone System
Capture/Record
Speech
Encode and
modulate
Replay Speech
Decode and
demodulate
Transmit
Receive
Radio
Channel

## Slide 3: Mobile Network Requirements
Admit users to the system
Keep track of their location
Divide resources between them efficiently
Direct them to the correct network, radio port, etc (c.f. handover)

## Slide 4: Network Functionalities
Radio Resource Management
  Power control
  Channel coding
  Handover
  Feed in to Admission Control
Mobility Management
  Location
  Roaming
Connection Management
  Call set up and termination
  Charging

## Slide 5: Network Functionalities
MM
MM
RM
RM
MM
Terminal
Radio
Access
Network
Core
Network
Network Manage-
ment System
CM
CM

## Slide 6: 1G Analogue Network
Mobile Telephone Switching Office
  All switching of calls to and from cells
  Blocking calls when congestion occurs
  Providing necessary backup to the network
  Monitoring the overall network elements
  Handling test and diagnostic capabilities of the system
PSTN
MTSO
HLR
BS
SIM
MS
VLR

## Slide 7: Basic GSM 2G Service
PSTN
ISDN
GMSC
MSC
VLR
NSS
BSS
EIR HLR AuC
BSC
BTS
SIM
MS

## Slide 8: System Components
HLR (Home Location Register)
  Storage and management of subscriptions
  Permanent data about subscribers
Mobile Switching Centre (MSC)
  Performs telephony switching functions
  Controls calls to and from the system
Visitor Location Register (VLR)
  Temporary data about subscribers
  Current location of mobile so it can be contacted

## Slide 9: System Components
Authentication Centre (AuC)
  Checks user’s identity
  Provides keys for confidentiality of each call
Equipment Identity Register (EIR)
  Information about terminal equipment
Base Station Controller (BSC)
  Controls handover and cell configuration
Base Transceiver Station (BTS)
  Physical transmission between the system and the mobile

## Slide 10: Network Structure
PSTN
ISDN
GMSC
BTS
MSC
BTS
BTS
BSC

## Slide 11: Value Added Services (e.g., SMS or Voice Mail)
VAS
PSTN
ISDN
GMSC
MSC
VLR
NSS
BSS
EIR HLR AuC
BSC
BTS
SIM
MS

## Slide 12: IN comes to 2G (Pay as You Go)
VAS
IN
PSTN
ISDN
GMSC
MSC
VLR
NSS
BSS
EIR HLR AuC
BSC
BTS
SIM
MS

## Slide 13: Additions for HSCSD (almost 2.5G)
VAS
IN
PSTN
ISDN
GMSC
MSC
VLR
NSS
BSS
EIR HLR AuC
BSC
BTS
SIM
MS

## Slide 14: Additions for GPRS (2.5G)
VAS
IN
Internet
(TCP/IP)
PSTN
ISDN
GMSC
MSC
VLR
NSS
BSS
GPRS Packet CN
EIR HLR AuC
BSC
BTS
SIM
MS
SGSN
GGSN

## Slide 15: Additions for E-GPRS (Almost 3G)
4
VAS
IN
Internet
(TCP/IP)
PSTN
ISDN
GMSC
MSC
VLR
NSS
E-RAN
E-GPRS Packet CN
EIR HLR AuC
BSC
BTS
SIM
MS
SGSN
GGSN

## Slide 16: 3G Release 99
VAS
CAMEL
Internet
(TCP/IP)
PSTN
ISDN
GMSC
MSC
VLR
Circuit Domain CN
E-RAN
Packet Domain CN
EIR HLR AuC
UTRAN
BSC
BTS
BS
RNC
USIM
SIM
USIM
SIM
SIM
MS
MS
MS
SGSN
GGSN
MExE

## Slide 17: 3G R4 The Move to All-IP
CAMEL
Internet
(TCP/IP)
MSC
Server
Circuit Domain CN
E-RAN
Packet Domain CN
Home Service Server
UTRAN
BSC
BTS
BS
RNC
USIM
SIM
USIM
SIM
SIM
MS
MS
MS
SGSN
GGSN
MExE
MGW
VAS
PSTN
ISDN
MGW
IP

## Slide 18: 3G R5 All-IP Arrives
CAMEL
Internet
(TCP/IP)
E-RAN
Packet Domain CN
Home Service Server
UTRAN
BSC
BTS
BS
RNC
USIM
SIM
USIM
SIM
SIM
MS
MS
MS
SGSN
GGSN
MExE
VAS
PSTN
ISDN
IP

## Slide 19: Future System Vision
High rate multimedia services
  High capacity requires smaller cells
  Global coverage very expensive
  Cells provided by local network operators
Increased service choice
  Greater number of services means larger number of service providers
  Increased competition forces down costs and is a requirement of regulators
Early example can be seen with MVNOs
Multiple air interfaces
  One size no longer fits all, again increasing network providers

## Slide 20: Diverse Networks
Dedicated Comms.
Device (Mobile
phone, etc)
Computing Device
(PC, PDA, etc)
Other consummer
devices
(entertainment, etc)
Personal Access
Networks (PAN,
Bluetooth, etc)
Local Area
Networks (WLAN,
HomeRF, etc)
Wide Area Networks
(2.5G, 3G cellular)
Service
User
Reconfigurable
network
Reconfigurable
terminal
Middleware
Service
Service
Future networks will have a multiplicity of different devices, interfaces and services
Middleware provides a framework to allow this to happen

## Slide 21: Requirements of the System
Mobile users should be able to:
discover the facilities available at their current location to allow them, or their service provider, to choose between them
select the most suitable air interface and protocol to access the service required
use the service, or application, in the same way wherever they may be
presume that their choices are secure in the most general sense
supported by VHE – OSA, MExE, STK in emerging specifications

## Slide 22: MVCE Research
Mobile VCE conducting research on next generation mobile systems
Designing a management framework with a focus on:
  Performance - how well do components, and systems built from them work?
  Integrity - do components, and systems built from them work at all?
  Security - are there threats latent in the distribution of objects, can interactions be subverted, can service be denied?

## Slide 23: What is Mobile VCE?
Research dedicated to Mobile and Personal Communications
A Collaborative Partnership
Virtual  distributed, making best use of individual partners’ skills
Undertaking longer-term pre-competitive research
Blending industrial and academic organisations (Board of Directors with Industrialists and Academics)

## Slide 24: Key Topic – Middleware
Define minimal functions required to facilitate communication and coordination between diverse devices
Security
Synchronisation
Discontinuous connection management
Communications paradigms
  messaging, caching, load balancing, proxying
Directory services
Notifications and events

## Slide 25: Key Topic – Mobile Agents
Decentralised, autonomous application components
Characterised
  Complex interrelationships transparent to physical location
  Possibly transient, discontinuous, long-term or short-term
  Aware of location and localised as necessary
Solutions
  Virtual network – for logical connectivity
  Active network – for resource management
Suitable for many but not all applications

## Slide 26
User
Service Provider
Comm System
technical
business
business
One Administrative Entity
S
S
S
N
N
N
M
L
M
C
User
Service Provider
business
MNO #1
MNO #1
MNO #1
DMP
technical
business
business
N Administrative Entities
Key Topic – Digital Marketplace

## Slide 27: Digital Marketplace Concept
Central trading entity to allow services and transport to be brokered
Mobiles access system by means for a control channel, can trade providers
Allows distributed system management and market entry by small players
Allows competition at a call or transaction level reducing subscriber costs
Generic framework required to allow trading across networks

## Slide 28: Accessing the Market
Mobiles access the market via a Logic Market Channel (LMC)
One LMC is provided in each communications technology traded in the market
LMCs are run by the Digital Marketplace
Users may use an LMC provided by one operator on behalf of the DMP to negotiate a contract with a different operator

## Slide 29: Trading in the Market
Negotiation by Contract
Generic parameters allow negotiation across networks : substitutability & complementarity
Performance parameters
    Bit rate
    BER
    Delay
Monitoring Parameters
    Degradation Allowance
    Sampling Rate
    Monitoring Period

## Slide 30: Verifying Conformance
In a radio system, individual users cannot verify conformance at a call level (a single contract is either fulfilled or not)
Market agent maintains independent record of conformance, termed a reputation
Service agents can examine the reputation of network operators when deciding contracts

## Slide 31: Conclusions
Significant trend towards networks based on All-IP
Services and mobile systems becoming more complex
Increasing complex middleware will interface services and transport
Systems beyond 3G will require a radically different business model
Transport is no longer the constraint in mobile networks