## Slide 1: Delivering Services in Next Generation Networks
Graham Clark
Product Strategy Consultant
Data, IP, and Voice Networks
Marconi Communications

## Slide 2: Overview
POTS Supplementary Services
IN Services
GSM and CAMEL
Into the Internet
WAP
Open Service API’s
Future Services
Future Applications
Summary

## Slide 3: POTS Supplementary Services
Wide range of services available to analogue and digital lines
All services delivered from the user’s local exchange
Local Exchange
(basic calls and services)
Data
Logic

## Slide 4: POTS Supplementary Services (2)
Analogue
  Largely operator or vendor defined
  No standard implementations
  Interactions resolved in code
  Knock on effects of introducing new services
Digital
  Some standardisation of services in ETSI
  Some standardisation of interaction requirements All services under the control of the network operator
Vendor works to operator requirements
Packaging of services determined by operator
Very limited user customisation

## Slide 5: Introduction of Intelligent Networks
Intelligent Networks introduced to enable fast roll out and support centralised services
Local or Trunk Exchange
Service Switching Point
Data
Logic
Service Control
Point
Service
Creation
INAP

## Slide 6: Intelligent Networks (2)
Routing and translation services delivered in the core of the network
User (line) related services delivered at the local service switching point, e.g. where the other user supplementary services are delivered
INAP is not an open network interface
Network operators remain in control of services
On-line user management of some services
Interactions controlled at the SSP (or SCP), including data driven techniques

## Slide 7: GSM and CAMEL
Visited
Mobile
Switch
Home Location
Register
Home CAMEL
Service Environment
CAP
MAP
To support international roaming plus supplementary services

## Slide 8: GSM and CAMEL (2)
GSM standard service set supported by all switching centres
Standard services available when roaming
Network specific services for differentiation, initially only within the home network
Introduction of CAMEL (mobile IN) to allow roaming with network specific services
CAP interface only open between network operators
Course standardisation of interaction between GSM services and CAMEL services
Home network operator remains in control

## Slide 9: Into the Internet
Two principle means of access
  From corporate IP networks via proxies and firewalls
  Via dial-up connection to ISP’s
Uni-directional service, i.e. access is user initiated
Service requires client applications in the user terminal (browser, mail, etc)
Except for the dial-up link to access an ISP, all flows are best effort
Telecomms operator controls dial-up link (e.g. POP selection)
ISP responsible for presentation of content

## Slide 10: Wireless Application Protocol
Web access from mobile phones
Enables presentation of Web content on a mobile phone display
GSM or GPRS
WAP Gateway
Web Server

## Slide 11: Wireless Application Protocol (2)
Controlled by a WAP Gateway
Gateway is aware of the terminal profile
Extension to provide WAP Telephony Applications
  scripted operations which execute within the terminal
  capabilities equivalent to a subset of INAP
  also terminal related operations (e.g. access to terminal phone book)
Full WTAI interface only available from trusted network gateways and servers
Other providers can only initiate call origination
Nature of WTAI avoids interactions

## Slide 12: Open Service API’s
Two possible models
  A network service using third party data
  A third party service using network resources
Local or Trunk Exchange
Service Switching Point
Data
Logic
SCP
SCP
3rd Party
3rd Party
Data
Logic
Mediation
API

## Slide 13: Open API’s (2)
Pressure from 3rd party organisations to access network resources
Regulatory and competitive issues
Revenue opportunities for operators and third parties
Requires security management to protect the integrity of the network
With a data API the network still controls the intention of the service, and can manage its interactions
A full service API removes detailed knowledge of the service from the network, and hence the granularity of interaction control

## Slide 14: Future Services
Are there new services at the connectivity level?
What delivery options?
Packet Access
Network
Packet Core
Network
Embedded
Services
Intelligent
Networks
WAP
3rd Parties
ISP
Terminal
Applications

## Slide 15: Future Services (2)
‘3rd Generation Networks’
Significant network changes
  Packet based networks
  ‘Always on’
  Terminal intelligence and capacity
  Bandwidth flexibility
Virtual Home Environment
  Utilising delivery mechanisms appropriate to the user location and current terminal equipment
  Intelligent services and intelligent service delivery
Conflicts of service interest
Who orders the chaos?
Who owns the user?

## Slide 16: Future Applications
Application vs Service
Rough definitions
  Applications are the reason for establishing communications - they are therefore related to the content being delivered
    Browsing
    Video
    E-commerce
  Services are the communications which support applications, including all the network, user, and terminal factors which affect the establishment of communication paths
    Number translations
    Call forwarding
  Applications use services

## Slide 17: Future Applications (2)
New application opportunities using QoS packet networks
More flexibility in the way applications use services
Service relationships can impact on applications
Add content providers to the list of players
How are all objectives to be met?
  Users want predictable behaviour from services and applications, customised to their preference
  Operators want revenues
  Providers want revenues and brand loyalty
  Clash of user preferences

## Slide 18: Summary (1)
Service delivery in the voice domain has progressed rapidly in the last 10 years
  Switch based
  Intelligent networks
  CAMEL
  WAP
Service delivery has remained essentially a network operator function
  Full knowledge of service intentions
  Defined points of control in the network
  Exceptions clearly bounded

## Slide 19: Summary (2)
Service provisioning and delivery is opening up
Packet networks, API’s, and intelligent terminals present new opportunities
Control is no longer concentrated on one equipment node or within one organisation
Assume nothing - anything is possible
QoS networks must offer more than ‘best-effort’ solutions to interactions
New challenges - new opportunities
Experience + innovation + vision
Reliability reputation revenue

## Slide 20
GRAHAM CLARK
Consultant
DATA, IP & VOICE NETWORKS
New Century Park
Coventry
United Kingdom
CV3 1HJ
Telephone: +44 (0)24 76 563911
Facsimile: +44 (0)24 76 563816
Email: graham.clark@marconicomms.com
www.marconicomms.com